Barrow Aerosol System

Daily Check Sheet

MON	TUE	WED	THU	FRI	MON	TUE	WED	THU	FRI

Date (UTC) 2007	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

Time (UTC)	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

Observer	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

From Computer

Laptop not frozen		 	 	 	 	 	 	 	 	 	 

Active filter #/Press.	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

(60-110 hPa)

Q_stack  700-800 lpm	 	 	 	 	 	 	 	 	 	 

Q_CNdrier ~7 lpm	 	 	 	 	 	 	 	 	 	 

Neph1 Lamp Voltage:	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

Neph1 Lamp Current:	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

CLAP Filter Transmission	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____ (Change if on filter #8)

Non-computer stuff:

PIDs meas’d~setpt 2&4 and 4f	 	 	 	 	 	 	 	 	 	 

CLAP Flow 0.9 lpm	 	 	 	 	 	 	 	 	 	 

Butanol lvl. 	 	 	 	 	 	 	 	 	 	 

Both CPC lites?	 	 	 	 	 	 	 	 	 	 

CNC Vac. > 12” Hg	 	 	 	 	 	 	 	 	 	 

Filter Vac. > 12” Hg	 	 	 	 	 	 	 	 	 	 

CO2 valve closed	 	 	 	 	 	 	 	 	 	 

UPS 	 	 	 	 	 	 	 	 	 	 

UMac green light on 	 	 	 	 	 	 	 	 	 	 

UMac yellow lights blinking 	 	 	 	 	 	 	 	 	 	 

Impactor: red or yellow lit 	R Y	R Y	R Y	R Y	R Y	R Y	R Y	R Y	R Y	R Y

SMPS sample flow 0.5 lpm         	 	 	 	 	 	 	 	 	 

SMPS sheath flow  5.0 lpm         	 	 	 	 	 	 	 	 	 

SMPS CPC butanol lvl.               	 	 	 	 	 	 	 	 	 

SMPS CPC lights?                       	 	 	 	 	 	 	 	 	 

CPC1 ~ CPC2

Periodic Stuff:

Neph Span Check, set CO2 flow at 8 lpm

CO2 tank pressure 	_____	_____		_____		_____	_____	_____		_____	_____	_____	_____

Neph error %		_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

Pump box Rotameters ~30 lpm	_____	_____		_____		_____	_____	_____		_____	_____	_____	_____

SMPS flow calibration

Carousel Change Time	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

(Thursday after 0Z)

Filters Activated?	 	 	 	 	 	 	 	 	 	 

Neph Impactor Change	_____	_____	_____	_____	_____	_____	_____	_____	_____	_____

Every few mths.

Notes: