# Text boxes

To CPC Inlet

Inlet Air

Sample Air

Sheath Air Flow (Moist Air)

Filter

0-10 lpm rotameter

Critical orifice

To vacuum pump

Sheath Air Flow (Dried Air)

Water drain line

Vessel filled w/ glass beads or commercial water trap

Refrigerator

Collection reservoir

Drain valve

¼” Swagelok tee

(stainless steel)

PermaPure Drier Tube

¼” Swagelok union

(stainless steel)