## Slide 1
The db system and data analysis tools
data extraction, averaging, exporting;
using templates for statistical analyses and plots,
documentation and FAQs

## Slide 2
Data extraction
How do I get data from one or more instruments into a data file?
Need to know what data you want!
(a) what instrument(s)?
(b) what averaging time?
(c) what processing (e.g., raw/edited)?
(d) what format?
How to figure out instrument names in the db system
data.instruments.get stn_id
station flow diagram
cpx2
Data Records and Data Variables
  http://www.esrl.noaa.gov/gmd/aero/software/aerosols/cpd2record.html
  http://www.esrl.noaa.gov/gmd/aero/software/aerosols/cpd2variables.html
Types of archives
Raw, edited, clean, averaged

## Slide 3
Tells you instrument ID, but not specific instrument…
CPX2 might help you figure out what instruments are what…

## Slide 4
Station flow diagram
ftp://ftp.cmdl.noaa.gov/aerosol/doc/drawings/stn/

## Slide 5
A11 N71 S11 A12 S12 A13
2009Q4 | | | |
2010Q1 | | | |
2010Q2 | | | |
2010Q3 | | | |
2010Q4 | | | |
2011Q1 | | | |
2011Q2 | | | | |
2011Q3 | | | | |
2011Q4 | | | | |
2012Q1 | | | | | |
2012Q2 | | | | | |
S11 2004-11-24T00:00:00Z TSI;3563;70417325: Installed
N71 2004-11-24T00:00:00Z TSI;3022;608: Installed
A11 2004-11-24T00:00:00Z Magee;Aethalometer-AE31;0202: Installed
A12 2006-05-27T00:00:00Z RR;PSAP-3W;92: Installed
S12 2011-04-10T00:00:00Z RR;M903;424: Installed
A13 2012-03-30T18:05:07Z GMD;CLAP-3W;18: Installed
Current Instruments:
S11 TSI;3563;70417325
N71 TSI;3022;608
A11 Magee;Aethalometer-AE31;0202
A12 RR;PSAP-3W;92
S12 RR;M903;424
A13 GMD;CLAP-3W;18
In a terminal window in Aer_vm, type:
data.instruments.get stn
Best way to figure out what’s what!
Where stn is your station’s 3-letter id (e.g., mlo, app, cpr, etc.)

## Slide 6
Record names in cpd2 and the DB-system
Two-part naming convention
First part is instrument identifier ("S11")
Second part is record type
  a high-frequency
  m monitor (low-frequency, housekeeping)
  r raw
  Others…
  Details at: http://www.esrl.noaa.gov/gmd/aero/software/aerosols/cpd2record.html
Most common record type to extract
Example: TSI Neph “S” records
a High frequency. Scattering, backscattering, temperature, RH and pressure.
m Low frequency. Status: voltages and reference.
s Statewise. Flags and status string.
c Zero results. Background
k Spancheck results.
So extracting “S11k” records would get nephelometer span check records

## Slide 7
Variable names in cpd2 and the DB-system
Two part names
  variable identifier
    first letter is variable category (e.g., "B", "N", “Q")
    various modifiers are used
      wavelength, size cut, and more…
  instrument identifier
    first character is instrument category ("S")
    second character is "line" identifier
    third character is sequence number in "line“
    BsG0_S11 = optical property scattering, green wavelength, 10um, neph S11
    BbsR_S12 = optical property backscattering, red wavelength, neph S12
    Q_A11 = flow, absorption instrument A11
  details at: http://www.esrl.noaa.gov/gmd/aero/software/aerosols/cpd2variables.html
Optical property
Number
Conc.
Flow

## Slide 8
raw - no corrections, no edits. Raw data exists as a physical archive.
edited - edits and corrections, but has not (necessarily) been approved and put into the clean archive. Edited data does not exist as a physical archive
clean - edits and corrections and has been approved by the station mentor. Clean data exists as a physical archive and is the source of most final data products.
avg[HDM] averaged clean data, excluding records flagged as contaminated, with one record for each hour/day/month, with everything on line one split on cut size, and including standard deviations and counts for each variable.
avgHe ,avgDe, avgMe
As above, except from edited data instead of clean. how to get averaged data with corrections applied even if you haven’t had a chance to edit it yet…
Types of data in the db system

## Slide 9
Where can I find help?
Software webpages:
http://www.esrl.noaa.gov/gmd/aero/software/aerosols/
(these webpages are also accessible under help menu on aer_vm)
Tutorial
  ftp://ftp.cmdl.noaa.gov/aerosol/doc/software/
  How_to_Get_Data_Out_of_the_Aero_Database.pptx
FAQ
  http://www.esrl.noaa.gov/gmd/aero/software/aerosols/dbfaq.htm

## Slide 10
HOW TO: Extract data in Excel format
Constant format files
  'xt2' creates files in comma-separated format with default name
  xt2 --header --clean -h cpr 2005 2006
  Makes a file called ‘al_HX.cpr’ in the current directory
  Advantages Disadvantages
  has neph, PSAP, CN data limited to neph, PSAP, CN
  always has same format limited to min., H, D, M
  simple to remember can’t use other data base tools

## Slide 11
HOW TO: Extract data in Excel format
New style "cpd2" formats
  Combine 'data.get' to select data with 'data.export' to get data file in desired format:
  data.get cpr S11a 2008:10 2008:11 | data.export --mode=excel > data.csv
“pipe”
station
record
Start time
End time
File format option
File name
db
command
db command
  Advantages Disadvantages
  data from any instrument complicated to remember
  any averaging time  format changes depending on instrument(s)
  can use db tools and extraction modes

## Slide 12
station
records
Start time
End time
File name
db
command
db command
  data.get cpr A11a,A12a 2008:10 5d clean |
  data.export --mode=excel --station=on --date-yeardoy=on > data.csv
HOW TO: Extract data in Excel format – getting fancy
File format option
pipe
Sometimes you want additional data in the file…
Sometimes you want different format…
Other file format options: http://www.esrl.noaa.gov/gmd/aero/software/aerosols/data.export.html
Can choose header, missing value code, flag format, date format, delimiter.

## Slide 13
Getting averaged data from db system
  data.get mlo S11a,A11a 2008:10 2008:11 avgH |
  data.export --mode=excel --station --date-fyear > data.csv
Hourly averaged data is easy!
How about 6h averages? Also easy!
data.avg --interval=6h --source=edited app S11a 2011:1 3d |
data.export --mode=excel > test_file
data.avg --interval=1m --stddev=off --count=off thd S11a 2010:1 1d raw |
data.consolidate --source=- --regex --noautoavg '.+[^0]_.+' |
data.export --mode=excel > test_file
Note: data.avg has other uses too:
How do I get 1min data for just one size cut? A bit more complex…
data.avg --stdev=off --count=off --interval=0 thd S11a 2010:1 1d raw |
data.export --mode=excel > test_file
Alternatively, this will give you both size cuts but in different columns:
Get data from hourly averaged archive
http://www.esrl.noaa.gov/gmd/aero/software/aerosols/data.avg.html

## Slide 14
DateTimeUTC,F1_A12,F1_A13,F2_A12,F2_A13,BaB0_A12,BaB0_A13,BaG0_A12,BaG0_A13,BaR0_A12,BaR0_A13,BaO0_A12,BaO0_A13,BaB1_A12,BaB1_A13,BaG1_A12,BaG1_A13,BaR1_A12,BaR1_A13,BaO1_A12,BaO1_A13,BaB0g_A12,BaB0g_A13,BaG0g_A12,BaG0g_A13,BaR0g_A12,BaR0g_A13,BaO0g_A12,BaO0g_A13,BaB1g_A12,BaB1g_A13,BaG1g_A12,BaG1g_A13,BaR1g_A12,BaR1g_A13,BaO1g_A12,BaO1g_A13,BaB0N_A12,BaB0N_A13,BaG0N_A12,BaG0N_A13,BaR0N_A12,BaR0N_A13,BaO0N_A12,BaO0N_A13,BaB1N_A12,BaB1N_A13,BaG1N_A12,BaG1N_A13,BaR1N_A12,BaR1N_A13,BaO1N_A12,BaO1N_A13,If1_A11,If2_A11,If3_A11,If4_A11,If5_A11,If6_A11,If7_A11,Ifz1_A11,Ifz2_A11,Ifz3_A11,Ifz4_A11,Ifz5_A11,Ifz6_A11,Ifz7_A11,Ip1_A11,Ip2_A11,Ip3_A11,Ip4_A11,Ip5_A11,Ip6_A11,Ip7_A11,Ipz1_A11,Ipz2_A11,Ipz3_A11,Ipz4_A11,Ipz5_A11,Ipz6_A11,Ipz7_A11,PCT_A11,Q_A11,X1c_A11,X2c_A11,X3c_A11,X4c_A11,X5c_A11,X6c_A11,X7c_A11,ZIr1_A11,ZIr2_A11,ZIr3_A11,ZIr4_A11,ZIr5_A11,ZIr6_A11,ZIr7_A11,Ff0_A12,Ff0_A13,Fn0_A13,IrB0_A12,IrB0_A13,IrG0_A12,IrG0_A13,IrR0_A12,IrR0_A13,L0_A12,L0_A13,Ff1_A12,Ff1_A13,Fn1_A13,IrB1_A12,IrB1_A13,IrG1_A12,IrG1_A13,IrR1_A12,IrR1_A13,L1_A12,L1_A13,If1g_A11,If2g_A11,If3g_A11,If4g_A11,If5g_A11,If6g_A11,If7g_A11,Ifz1g_A11,Ifz2g_A11,Ifz3g_A11,Ifz4g_A11,Ifz5g_A11,Ifz6g_A11,Ifz7g_A11,Ip1g_A11,Ip2g_A11,Ip3g_A11,Ip4g_A11,Ip5g_A11,Ip6g_A11,Ip7g_A11,Ipz1g_A11,Ipz2g_A11,Ipz3g_A11,Ipz4g_A11,Ipz5g_A11,Ipz6g_A11,Ipz7g_A11,PCTg_A11,Qg_A11,X1cg_A11,X2cg_A11,X3cg_A11,X4cg_A11,X5cg_A11,X6cg_A11,X7cg_A11,ZIr1g_A11,ZIr2g_A11,ZIr3g_A11,ZIr4g_A11,ZIr5g_A11,ZIr6g_A11,ZIr7g_A11,Ff0g_A12,Ff0g_A13,Fn0g_A13,IrB0g_A12,IrB0g_A13,IrG0g_A12,IrG0g_A13,IrR0g_A12,IrR0g_A13,L0g_A12,L0g_A13,Ff1g_A12,Ff1g_A13,Fn1g_A13,IrB1g_A12,IrB1g_A13,IrG1g_A12,IrG1g_A13,IrR1g_A12,IrR1g_A13,L1g_A12,L1g_A13,F2N_A12,F2N_A13,If1N_A11,If2N_A11,If3N_A11,If4N_A11,If5N_A11,If6N_A11,If7N_A11,Ifz1N_A11,Ifz2N_A11,Ifz3N_A11,Ifz4N_A11,Ifz5N_A11,Ifz6N_A11,Ifz7N_A11,Ip1N_A11,Ip2N_A11,Ip3N_A11,Ip4N_A11,Ip5N_A11,Ip6N_A11,Ip7N_A11,Ipz1N_A11,Ipz2N_A11,Ipz3N_A11,Ipz4N_A11,Ipz5N_A11,Ipz6N_A11,Ipz7N_A11,PCTN_A11,QN_A11,X1cN_A11,X2cN_A11,X3cN_A11,X4cN_A11,X5cN_A11,X6cN_A11,X7cN_A11,ZIr1N_A11,ZIr2N_A11,ZIr3N_A11,ZIr4N_A11,ZIr5N_A11,ZIr6N_A11,ZIr7N_A11,Ff0N_A12,Ff0N_A13,Fn0N_A13,IrB0N_A12,IrB0N_A13,IrG0N_A12,IrG0N_A13,IrR0N_A12,IrR0N_A13,L0N_A12,L0N_A13,F1N_A12,F1N_A13,Ff1N_A12,Ff1N_A13,Fn1N_A13,IrB1N_A12,IrB1N_A13,IrG1N_A12,IrG1N_A13,IrR1N_A12,IrR1N_A13,L1N_A12,L1N_A13
data.get cpr A11a,A12a,A13a 2012:116 1d avgHe | data.export --mode=excel > test_file

## Slide 15
DateTimeUTC,BaB0_A12,BaG0_A12,BaR0_A12,BaO0_A12,BaB1_A12,BaG1_A12,BaR1_A12,BaO1_A12,BaB0g_A12,BaG0g_A12,BaR0g_A12,BaO0g_A12,BaB1g_A12,BaG1g_A12,BaR1g_A12,BaO1g_A12,BaB0N_A12,BaG0N_A12,BaR0N_A12,BaO0N_A12,BaB1N_A12,BaG1N_A12,BaR1N_A12,BaO1N_A12
data.consolidate --source=avgH cpr 115 116 'Ba*_A12' | data.export --mode=excel > myfile
How do I get only absorption and not any of the crazy variables that I won’t look at anyway?
POP-QUIZ!
What does variable BaR0_A12 represent??
What about BaO0g_A12?

## Slide 16
JulianDay:0 Year:1 DOY:2 F1_A12_Bit0:3 F1_A12_Bit1:4 F1_A12_Bit2:5 F1_A12_Bit3:6 F1_A12_Bit4:7 F1_A12_Bit5:8 F1_A12_Bit6:9 F1_A12_Bit7:10 F1_A12_Bit8:11 F1_A12_Bit9:12 F1_A12_Bit10:13 F1_A12_Bit11:14 F1_A12_Bit12:15 F1_A12_Bit13:16 F1_A12_Bit14:17 F1_A12_Bit15:18F2_A12_Bit0:19 F2_A12_Bit1:20 F2_A12_Bit2:21 F2_A12_Bit3:22 F2_A12_Bit4:23 F2_A12_Bit5:24 F2_A12_Bit6:25 F2_A12_Bit7:26 F2_A12_Bit8:27F2_A12_Bit9:28 F2_A12_Bit10:29 F2_A12_Bit11:30 F2_A12_Bit12:31 F2_A12_Bit13:32 F2_A12_Bit14:33 F2_A12_Bit15:34 BaB0_A12:35 BaB0_A12_MVC:36BaG0_A12:37 BaG0_A12_MVC:38 BaR0_A12:39 BaR0_A12_MVC:40 BaO0_A12:41 BaO0_A12_MVC:42 BaB1_A12:43 BaB1_A12_MVC:44 BaG1_A12:45 BaG1_A12_MVC:46 BaR1_A12:47 BaR1_A12_MVC:48 BaO1_A12:49 BaO1_A12_MVC:50 BaB0g_A12:51 BaB0g_A12_MVC:52 BaG0g_A12:53 BaG0g_A12_MVC:54 BaR0g_A12:55 BaR0g_A12_MVC:56 BaO0g_A12:57 BaO0g_A12_MVC:58 BaB1g_A12:59 BaB1g_A12_MVC:60 BaG1g_A12:61 BaG1g_A12_MVC:62 BaR1g_A12:63 BaR1g_A12_MVC:64 BaO1g_A12:65 BaO1g_A12_MVC:66 BaB0N_A12:67 BaB0N_A12_MVC:68 BaG0N_A12:69 BaG0N_A12_MVC:70 BaR0N_A12:71 BaR0N_A12_MVC:72 BaO0N_A12:73 BaO0N_A12_MVC:74 BaB1N_A12:75 BaB1N_A12_MVC:76 BaG1N_A12:77 BaG1N_A12_MVC:78 BaR1N_A12:79 BaR1N_A12_MVC:80 BaO1N_A12:81 BaO1N_A12_MVC:82 Ff0_A12:83 Ff0_A12_MVC:84 IrB0_A12:85 IrB0_A12_MVC:86 IrG0_A12:87 IrG0_A12_MVC:88 IrR0_A12:89 IrR0_A12_MVC:90 L0_A12:91 L0_A12_MVC:92 Ff1_A12:93 Ff1_A12_MVC:94 IrB1_A12:95 IrB1_A12_MVC:96 IrG1_A12:97 IrG1_A12_MVC:98 IrR1_A12:99 IrR1_A12_MVC:100 L1_A12:101 L1_A12_MVC:102 Ff0g_A12:103 Ff0g_A12_MVC:104 IrB0g_A12:105 IrB0g_A12_MVC:106 IrG0g_A12:107 IrG0g_A12_MVC:108 IrR0g_A12:109 IrR0g_A12_MVC:110 L0g_A12:111 L0g_A12_MVC:112 Ff1g_A12:113 Ff1g_A12_MVC:114 IrB1g_A12:115 IrB1g_A12_MVC:116 IrG1g_A12:117 IrG1g_A12_MVC:118 IrR1g_A12:119 IrR1g_A12_MVC:120 L1g_A12:121 L1g_A12_MVC:122 F2N_A12:123 F2N_A12_MVC:124 Ff0N_A12:125 Ff0N_A12_MVC:126 IrB0N_A12:127 IrB0N_A12_MVC:128 IrG0N_A12:129 IrG0N_A12_MVC:130 IrR0N_A12:131 IrR0N_A12_MVC:132 L0N_A12:133 L0N_A12_MVC:134 F1N_A12:135 F1N_A12_MVC:136 Ff1N_A12:137 Ff1N_A12_MVC:138 IrB1N_A12:139 IrB1N_A12_MVC:140 IrG1N_A12:141 IrG1N_A12_MVC:142 IrR1N_A12:143 IrR1N_A12_MVC:144 L1N_A12:145 L1N_A12_MVC:146
data.get cpr A12a 115 116 avgHe | data.export --mode=idl > test_file
Tells you what columns data are in, file has no header
Splits flags column into individual bits
I don’t use excel…microsoft is the evil empire!

## Slide 17
All those useful intensive parameters… single scattering albedo, Ångström exponent, etc.
Do I really have to do the calculations myself?
Nope…there’s a script for that!
data.aggregate.intensives sgp XIs 2008:10 2008:11
Intensive parameters – can I get those too?
XIs is the ‘short’ intensives record - mostly properties at 550 nm + blue/red Ångström exponent
XIl is the ‘long’ intensives record – properties at all the wavelengths
http://www.esrl.noaa.gov/gmd/aero/software/aerosols/cpd2variables.html#intensives_record
Go here to see specifically what is in the intensives record:

## Slide 18
I’ve made this data file – Now what?
Move it from the AER_VM to your computer and do with it what you will…
--excel
--idl
--matlab , igor, …
--send it to someone…
Another option:
Use ‘R’ scripts on AER_VM to make several ‘canned’ statistical plots
Scripts are in /aer/prg/r/ and /aer/prg/r/examples/
Some useful scripts are:
density-plot.r
multi-station-box-month.r
quantile.r
Note: the R scripts are set up to do the data extraction also – so you don’t need to extract data before using the scripts – you need to edit the script to tell it what data to extract...

## Slide 19
This is the stuff you can change to get the plot you want
There is more stuff further down in the script that can be changed too.
This is what you type to run the script

## Slide 21
Modifying the R script
OLD
NEW

## Slide 23
Opening the script to edit it on AER_VM
use nedit or vi
e.g., type: nedit multi-station-box-month.r <enter>
The pound symbol “#” in an R script indicates a comment – the computer ignores everything on the same line after a ‘#’
Getting help with some basic R
Get an ‘R’ book
using the ‘R’ documentation online info:
type: R <enter> at a command line prompt in a AER_VM terminal
then type the name of the command you need help with
for example
type: ?POSIXlt <enter> at the prompt in the R interface to see stuff about time
or
type: ?read.csv<enter> to see stuff about reading files
to get out of the R interface:
type: q() <enter>
Get a Derek  (can’t have ours!)
Practical R stuff

## Slide 24
density-plot.r - generates xy-scatter plot showing relation between two variables and population density of points
[1] "STN" "Variable" "0.01" "0.05" "0.1" "0.25" "0.5" "0.75" "0.9" "0.95" "0.99"
[1] "bnd" "BsG0_S11" "21.177" "23.67" "28.75" "36.99" "48.25" "52.33" "54.56" "56.45" "59.14"
quantiles.r - outputs percentiles and median of a variable
Other scripts

## Slide 25
When you submit data to the WDCA, where does it go?
Website:
ebas.nilu.no
Note: website is painfully slow. Need to be patient.
- Public data
Most of the data stored in EBAS are originating from programs encouraging an unlimited and open data policy for non-commercial use. For scientific purposes, access to these data is unlimited and provided without charge. By their use you accept that an offer of co-authorship will be made through personal contact with the data providers or owners whenever substantial use is made of their data. In all cases, an acknowledgement must be made to the data providers or owners and to the project name when these data are used within a publication. Public data are available without login.

## Slide 26
How do I get data out of the WDCA?
To get to this page need to click ‘accept terms’ on start-up page.
Data policy is also here

## Slide 27
Select group to get all parameters
Select date range
Download!

## Slide 28
To get NOAA & NOAA collaborator data
Pick country (USA, Canada, etc.)
Pick station in country
Pick sizecut (PM1, PM10)

## Slide 29
There will be one file for each year, size cut, and instrument.
If it’s NOAA collaborator file, the header will be huge and descriptive.
The data files will have consistent format from year to year (so long as there wasn’t an instrument change).
If you download data from a non-NOAA site the header may not be as informative.
Non-NOAA station files may switch format from year to year. You will need to look in the header to see what data are in what column.
Info/Caveats about data downloaded from NILU/EBAS
PR0100C.20080101000000.20120201192555.aerosol_light_scattering_coefficient.pm10.1y.1h.lev2.nas
PR0100C.20080101000000.20120201192555.aerosol_light_scattering_coefficient.pm1.1y.1h.lev2.nas
PR0100C.20090101000000.20120201194805.aerosol_light_scattering_coefficient.pm10.1y.1h.lev2.nas
PR0100C.20090101000000.20120201194805.aerosol_light_scattering_coefficient.pm1.1y.1h.lev2.nas
PR0100C.20100101000000.20120202190241.aerosol_light_scattering_coefficient.pm10.1y.1h.lev2.nas
PR0100C.20100101000000.20120202190241.aerosol_light_scattering_coefficient.pm1.1y.1h.lev2.nas
PR0100C.20110101000000.20120201160604.aerosol_light_scattering_coefficient.pm10.1y.1h.lev2.nas
PR0100C.20110101000000.20120201160604.aerosol_light_scattering_coefficient.pm1.1y.1h.lev2.nas
Example list of TSI neph files for a station: