Meteorological data from the 1994 UV-B Spectroradiometer 
Intercomparison held at the Table Mountain Test Facility Boulder, 
Colorado September 17-October 1, 1994.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_94/met
directory.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as MET###.TXT, where ### refers to the Julian date, 
contain the meteorological data from the met tower for the days that 
solar spectral scans were taken during the intercomparison.  The data 
in the files is in processed form.  The calibration factors to be applied 
to the data are listed below.

Files listed as MET###.XLS are saved in EXCEL 5.0c format.

The description of the data files is as follows;

Line out from logger, Year, Julian date, HourHourMinuteMinute (GMT), 
Barometric Pressure, Temperature, Relative Humidity, Wind Speed, and
Wind Azimuth.

The calibration factors are,

Wind speed                        calibrated in Meters/Second

Wind direction                  calibrated in degrees clockwise from due North

Temperature                      calibrated in degrees Celsius

Relative Humidity             calibrated in percent (%) relative humidity

Barometric Pressure        readings in mVolts.  Calibration transfer coefficient
1.086 mBarr/mV             (Calibration factor obtained through transfer from 
Precision Aneroid Barometer, Model # MK2 serial # D196)