Yankee Environmental Systems UVB-1 radiometer data from the 1995 
UV-B Spectroradiometer Intercomparison held at the Table Mountain 
Test Facility Boulder, Colorado June 14-23, 1995.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_95/yankee
directory.
These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as YES###.TXT, where ### refers to the Julian date, 
contain the broadband UVB data from the Yankee UVB-1's for the 
days that solar spectral scans were taken during the intercomparison. 
The data in the files is in raw form as logged from the instrument in mV.
The calibration factor to be applied to the data is listed below.

The description of the data files is as follows;

Line out from logger, Year, Julian date, HourHourMinuteMinute (GMT), 
Yankee UVB-1 (serial #940401), Yankee UVB-1 (serial # 940402), 
Yankee UVB-1 (serial # 940404), the next three columns are the 
respective temperature resistances, and then the next six columns are the 
respective standard deviations of the three Yankee's and the temperature 
resistances.

The files listed as YANK###.TXT are the data files with the Unweighted
Irradiance conversion factor applied.

The files listed as YANK###.XLS are the same as the files YANK###.TXT
but are saved in EXCEL 5.0c format.  Included is a plot of the Unweighted 
Irradiance.


The calibration factor for all Yankee UVB-1's is,

Calibration Factor  (1/1000)V/mV*(2*data(mV))*1.97(W/mE2)/V  
for TOTAL UVB 280-320 nm

Calibration Factor  (1/1000)V/mV*(2*data(mV))*0.136(W/mE2)/V 
@45-50 degrees solar zenith angle for Diffey Weighted Irradiance.