Normal Incidence Pyrheliometer (NIP) data from the 1994 UV-B 
Spectroradiometer Intercomparison held at the Table Mountain 
Test Facility Boulder, Colorado September 17-October 1, 1994.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_94/nip
directory.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as NIP###.TXT, where ### refers to the Julian date, 
contain the pyrheliometer data from the NIP instrument for the days 
that solar spectral scans were taken during the intercomparison.  The 
data in the files is in processed form.  The calibration factor applied 
to the data is listed below.

Files listed as NIP###.XLS are saved in EXCEL 5.0c format.

The description of the data files is as follows;

Year, Julian date, HourHourMinuteMinute (GMT), 
NIP raw data (in mV), Time Decimal GMT, Calibrated data (in W/mE2).

The calibration factor is,

(data*(1/1000)V/mV)/8.110E-6 V/(W/mE2)