Spectrosun Solar Pyranometer (PSP) data from the 1994 UV-B 
Spectroradiometer Intercomparison held at the Table Mountain 
Test Facility Boulder, Colorado September 17, October 1, 1994.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_94/psp
directory.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as PSP###.TXT, where ### refers to the Julian date, contain 
the ancillary data from the PSP's for the days that solar spectral scans were 
taken during the intercomparison.  The data in the files is in raw form as 
logged from the instrument in mV.  The calibration factors to be applied to 
the data are listed below.

Files listed as PSP###.XLS are saved in EXCEL 5.0c format.

The description of the data files is as follows;

Year, Julian date, HourHourMinuteMinute (GMT), PSP 
(serial # 73-38), PSP (serial # 73-44), PSP (serial # 73-99), 
the next three columns are the respective standard deviations of 
the three PSP's.

The calibration factors are to be used for the data files listed in mV,

Convert the data in mVolts to Volts by multiplying (1/1000)V/mV
first before applying the calibration factors.

PSP Serial Number   Calibration Factor (x 10E-6 V/(WmE-2))

73-38                                                 9.68
73-44                                                 8.71
73-99                                                 9.63