Meteorological data from the 1995 UV-B Spectroradiometer 
Intercomparison held at the Table Mountain Test Facility 
Boulder, Colorado June 14-23, 1995.

Latitude:       40.125 degrees North
Longitude:   105.237 degrees West
Elevation:    1,689 m


The files listed as MET###.TXT, where ### refers to the Julian 
date, contain the meteorological data from the met tower for the 
days that solar spectral scans were taken during the intercomparison.
The data in the files is in raw form as logged from the instruments 
in fifteen minute averages.  The calibration factors to be applied to 
the data are listed below.

The description of the data files is as follows;

Line out from logger, Year, Julian date, HourHourMinuteMinute 
(GMT), Temperature, Relative Humidity, Wind Speed, Wind 
Azimuth, Barometric Pressure, and then the next five columns are 
the respective standard deviations of the temperature, relative 
humidity, wind speed, wind azimuth, and pressure.

The calibration factors are,

Wind speed                        calibrated in Meters/Second

Wind direction                  calibrated in degrees clockwise from due North

Temperature                      calibrated in degrees Celsius

Relative Humidity             calibrated in percent (%) relative humidity

Barometric Pressure        readings in mBars;  calibration factor 0.999766 to 
be applied to readings (Calibration factor obtained through transfer from 
Precision Aneroid Barometer, Model # MK2 serial # D196)