## Slide 1
Exploring causes of low single scattering albedo during autumn in central North America
Elisabeth Andrews and Erin Boedicker
University of Colorado, Boulder, USA
NOAA/Global Monitoring Laboratory, Boulder USA
USGS national map
BND (Bondville, IL)
5 km
Notes: Aerosol measurements established 1994. Wind from west hemisphere, highest prevalence SSW, followed by NW (extra slide). Site is ~20km from champaign-urbana (pop ~100k)

## Slide 2
Introduction
Single scattering albedo (SSA) at BND is lower in September and October.
1996-2001 D&O
2010-2013 Sherman
2014-2023 Last 10 y
Single scattering albedo
D&O=Delene and Ogren, JAS, 2002
Sherman=Sherman et al., ACP, 2015
Several hypotheses have been proposed:
Preferential scavenging of scattering aerosol by precipitation (Sherman et al., 2015)
Biomass burning (Buzcu-Guven et al., 2007)
Agricultural harvest activities (Delene and Ogren, 2002)
WHY???
Notes: CC 2020 – slight decreasing trend in SSA (getting slightly darker) between -0.0005 and 0 annually and summer (other seasons no SS trend)

## Slide 3
Site Measurements
In-situ aerosol system
Measurement | Institute
Aerosol optical properties | NOAA GML, since 1994
Meteorology (RH, Wind, etc.) | NOAA/GML, since 1994
Aerosol chemistry | NOAA/PMEL, 1994-2008
Carbon monoxide | US EPA, 2012-2018
Precipitation | Illinois Climate Network, since 1990 NOAA Online Weather, since 1995
Soil Moisture | Illinois Climate Network, since 2012
Other measurements at BND include:
NASA AERONET
NADP precipitation chemistry
IMPROVE aerosol chemistry
US EPA dry deposition chemistry, PM2.5, AQ gases
SURFRAD solar radiation
USDA UV-b radiation
https://www.isws.illinois.edu/climate-and-atmospheric-science/bondville-environmental-and-atmospheric-research-site

## Slide 4
Is wet scavenging causing low SSA at BND?
Relative humidity is low in September and October
Precipitation is also low in September and October
September/October SSA is lower than other months regardless of RH
Single scattering albedo
Relative humidity (%)
NOAA/GML
No indication that wet removal is causing the low SSA.
Ambient RH (%)
Monthly Precipitation (in)
Foggy October day at BND

## Slide 5
Is biomass burning causing low SSA at BND?
September/October fires
NW fires are likely forest fires
SW fires are likely agricultural burning
US fires by month (MODIS data 2017)
Jaffe et al, JAWMA, 2020
SSA<0.90 (113 traj)
SSA>0.95 (35 traj)
5 day back trajectories,
NCEP/NCAR Reanalysis for 2012-2017
Median back trajectories for September & October
Both trajectories could perhaps transport smoke to BND
NW trajectory associated with low SSA
Notes: Traj met data has 2.5x2.5 degree spacing

## Slide 6
Pollution rose of co-albedo (1-SSA)
NOAA/GML wind and aerosol data (2012-2023)
September
October
Potassium – elevated in September & October
CO – elevated in September, low in October
Biomass burning markers
Potassium is PM1 data from NOAA/PMEL (1995-2008)
Carbon monoxide data is from US EPA (2012-2018)
Is biomass burning causing low SSA at BND?
No clear chemical signal for BB
No clear local source of darker aerosol
Potassium
Carbon monoxide
Local winds more easterly for low albedo (high co-albedo) but contributions from all directions
mg/m3
Notes: Traj for SSA<0.85 and 0.85<SSA<0.9 look similar to SSA<0.9,

## Slide 7
Are agricultural harvest activities causing low SSA at BND?
Soil markers
Calcium
Potassium
Magnesium
Ion data is PM1 data from NOAA/PMEL (1995-2008)
All three soil markers are elevated in Sept. & Oct.
No increase in soil markers during April
BND has enhanced soil loading during spring planting and fall harvesting. (Malm et al., 2007).
Chemistry measurements suggest increased soil source in September/October
Harvest day in northern Illinois
Photo by Ira Block
mg/m3
Notes: Malm suggests highest soil loading in spring (April).

## Slide 8
Are agricultural harvest activities causing low SSA at BND?
NOAA GML aerosol data (2012-2023)
SSA
Illinois corn planting and harvesting schedule
Weekly SSA and Scattering Angstrom exponent
Sept./Oct. decrease in SSA is consistent with regional harvest emissions
Soil signal in April during planting is not as strong
Corn and soybean crop schedules suggest harvesting occurs from mid-September to late October
SSA and SAE decrease as harvesting increases indicating larger, darker particles
Crop progress and condition charts
SAE
J F M A M J J A S O N D
Notes: Could be some diesel from harvesters contributing to SSA decrease, but don’t see increase in CN or clear change in AAE.

## Slide 9
Why isn’t SSA low at BND during spring agricultural activities?
Coarse mass soil loading near BND is higher in fall than in spring. (Hand et al., 2019)
Highest in April during planting
Lowest in September and October during harvest.
Dry soil in autumn leads to more dust emission than in spring when soil is moist?
ISWS, Illinois Climate Network
BND soil moisture
BND

## Slide 10
Take-aways
Wet scavenging and biomass burning seem unlikely to cause the low SSA at BND in September and October.
Low SSA at the site is likely related to harvesting activities combined with dry soil.
Other intensive agricultural activities (planting) appear to have less impact on SSA, possibly due higher soil moisture content.

## Slide 11
Future work
Explore SSA decrease across central North American sites
Investigate correlations between soil moisture and aerosol optical properties
Perform PMF analysis to identify sources impacting site
Source apportionment of absorbing aerosol using spectral absorption data
Review literature on optical properties of non-desert soils
Evaluate CLAP fllters using SEM
BND
WPB
EGB
PM1
PM10
Image courtesy of Andras Vlader at NIST and Adam Deitsch SUNY-Albany
CLAP filter from BND, April 9, 2018

## Slide 12
Extra slides

## Slide 13
Monthly stats for aerosol optical properties. Red=PM10, Blue=PM1

## Slide 14
Monthly stats for basic meteorological data (GML measurements)

## Slide 15
Aerosol property interannual variability over 10 years at BND

## Slide 16
Ambient RH
Aerosol property variability with RH at BND

## Slide 17
Wind is primarily from the south and west, though it changes with month.

## Slide 18
Absorption wind rose
Scattering wind rose
Sherman et al., 2015

## Slide 19
Hand et al 2019

## Slide 20
Motivation
Sheridan et al., 2012