## Slide 1
A general introduction into aerosols
Elisabeth Andrews
CATCOS Aerosol Workshop, June 2016

## Slide 2
What’s an Aerosol?
Definition: Particle or liquid suspended in a gas.
Examples of atmospheric aerosols:
  Dust
  Combustion aerosol (forest fires, vehicles…)
  Sea salt
  Pollen
  Pollution particles (e.g., sulfates, nitrates, organics…)
Natural and man-made

## Slide 3
Primary particles – directly emitted by a source in particle form
Secondary particles – particulate material formed in atmosphere
What’s an Aerosol?
Gas phase
molecules
Molecular
Cluster
Detectable
Particle
Nucleation
Condensation
Gas phase
molecules
Existing particle
or
Examples of secondary aerosol formation:

## Slide 4
Examples of Aerosol Particles
Aerosol Characteristics
Size
Composition
Shape

## Slide 5
Particle properties – Amount
Different ways of describing aerosol amount:
Mass concentration
Extinction (visibility)
Aerosol optical depth
Colorado from: http://vista.cira.colostate.edu/views/
sext = 20 Mm-1
sext = 200 Mm-1
Hanoi
Liuzhou
Beihai
Wuxu
600
500
400
300
200
100
Extinction (Mm-1)
Visibility (km)
6
10
20
40
15
8
Bulk
From: capita.wustl.edu

## Slide 6
Particle properties – Mass Concentration
Particulate Material (PM) = mass of aerosol particles/sample vol.
bulk property (integrated over time, size, composition)
      PM is often designated by size:
      TSP (total suspended particulate, no size cut)
      PM10 (particles with diameter < 10 mm)
      PM2.5 (particles with diameter < 2.5 mm)
Co et al., 2013
Sept-Oct
Wet season
Dec-Jan
Dry season
April
Transitional
PM mass concentration

## Slide 7
Particle properties – SIZE
Importance of aerosol size
Influences the optical properties of particles
absorption
scattering
Affects transport and lifetime
large particles removed from atmosphere more quickly
smaller particles transported farther
Impacts health and welfare
determines respiratory system deposition
Size varies with:
Location
Time
Source/composition

## Slide 8
Particle properties – SIZE
How big are atmospheric particles?
Diameter ~ 0.01-100 mm
PM2.5
Diameter<2.5 mm
PM10
Diameter<10 mm
Human hair
Diameter~70 mm
Fine beach sand
Diameter~90 mm
From USEPA

## Slide 9
Particle properties – SIZE
How big are atmospheric particles?
Diameter ~ 0.01-100 mm
http://binational.pharmacy.arizona.edu/content/mine-tailings
Gas-to- particle
(nucleation
Molecular cluster
virus
bacteria
dust
pollen
Sea salt
Rain drops
Fog

## Slide 10
1 mm
10 mm
0.1 mm
0.01 mm
0.001 mm
Particle Diameter
Particle properties – SIZE
PM10
PM2.5
Size of particles determined by source and formation processes.
Size distribution of atmospheric particles covers wide size range.
http://www.dwd.de/EN/research/observing_atmosphere/composition_atmosphere/aerosol/cont_nav/particle_size_distribution_node.html

## Slide 11
Different parts of the size distribution are important for different processes and effects.
Volume/Mass
Surface area/Scattering
Number
Amount
SIZE
Examples:
Health effects (respiratory issues) primarily depend on particles < 2.5 mm.
Optical properties (visibility) primarily depend on particles > 0.1 mm.
Particle mass fluxes (deposition) primarily depend on particles > 1 mm.
PM10 is dominated by coarse mode
Measurement technique should be based on application.
http://elte.prompt.hu/sites/default/files/tananyagok/AtmosphericChemistry/ch09s02.html
Particle properties – SIZE

## Slide 12
From ‘Deposition of inhaled particles in the human respiratory tract and consequences for regional targeting in respiratory drug delivery, Joachim Heyder
Particle Diameter (mm)
Deposition Fraction
Particle properties – SIZE
Particle size determines if/where particles deposit in the respiratory system.
Small particles (Diameter < 0.1 mm) are more likely to end up deep in the lungs

## Slide 13
Particle properties – COMPOSITION
Importance of aerosol composition
Provides indicator of sources contributions
Influences the optical properties of particles
absorption
scattering
Affects aerosol/water interactions
water uptake changes size, optical properties
fog/cloud drops
Impacts health and welfare
acid rain/deposition
determines toxicity
Composition varies with:
Location
Particle size
Time
Sources

## Slide 14
Particle properties – COMPOSITION
Organic
Nitrate (NO3)
Ammonium (NH4)
Sulfate (SO4)
DATE, 2012
Concentration
February
March
April
DOE/ARM
Composition varies with time at same location
Study mean

## Slide 15
Huang et al., Nature 2014
Particle properties – COMPOSITION
Different locations have different chemical composition
Source contributions influence chemical composition

## Slide 16
Cohen et al (2010)
Air mass trajectories corresponding to desert dust reaching Hanoi
Air mass trajectories corresponding to coal power plant emissions reaching Hanoi
Particle properties – COMPOSITION
Aerosol can be transported over large distances.
Source region will affect aerosol composition.

## Slide 17
Delhaye, 2009
Ogren & Charlson 1983
Soto, 2008
Defined by five properties:
  Composition
  Morphology (shape)
  Volatility
  Solubility
  Light absorption (optical)
Particle properties – COMPOSITION
Black carbon (BC) has important effects on climate and health.
BC is primary absorbing aerosol in atmosphere
BC is poorly defined in the scientific literature.
BC amounts depend on the measurement method.

## Slide 18
Particle properties – COMPOSITION
Different types of aerosol in different places.
Black carbon
Soil dust
Sulfate
Sea salt
From SPRINTARS model

## Slide 19
Finlayson-Pitts and Pitts, 2000
Composition dependent size distribution
(urban aerosol)
Friedlander, 2000
Source dependent size distribution
(continental and marine aerosol)
Amount
Amount
PM1
PM10
PM1
Particle properties – SIZE+CHEMISTRY
Different types of aerosol will have different size distributions
Size distribution chemistry varies with size

## Slide 20
Park and Son, 2015
Particle properties – MASS+SIZE+CHEMISTRY
PM10
February 2015
Diameter (um)
mass concentration
No dust
Dust
Diameter (um)
Chemical mass concentration
Chemical mass concentration

## Slide 21
University of Bristol
Particle properties – CHEMISTRY and water
Zieger et al., 2014
Particles interact with water vapor (relative humidity) in the atmosphere
change size
change composition
change optical properties
Different types of particles interact differently with water

## Slide 22
Climate
Visibility
Health/
Welfare
Optical
Properties
Scattering,
absorption,
phase function
Chemical
Properties
Hygroscopicity,
toxicity
Physical
Properties
Size, shape, amount
In-situ Aerosol
Monitoring
It’s all tied together!

## Slide 23
Not used slides

## Slide 24
Sulfate, Xu and Penner, 2012
Number, Spracklen et al., 2010
Black carbon, Skeie et al., 2011
Dust, Jickells et al., 2005
Particle properties – COMPOSITION
Different types of aerosol in different places.
Annual mean values
Various models

## Slide 25
Relative Humidity (%)
Radiative forcing efficiency (W m-2 AOD-1)
Depending on aerosol, humidity can have strong influence on aerosol optical properties and radiative forcing.
Humidity dependence can vary by site and by season.
Scat(85%)/scat(40%)
Long term is important!!
Particle properties – CHEMISTRY and water

## Slide 26
http://capita.wustl.edu
How separate out?
Don’t need complex chem?

## Slide 27
Max planck inst.
John wenger university college cork

## Slide 28
Measured Parameters
Clean Region: 10 Mm-1 < Light extinction
Polluted Region: Light extinction > 60 Mm-1
Boulder: light extinction ~10-20 Mm-1
These properties depend on AMOUNT of Aerosol:
Light absorption, sap
Light scattering, ssp
Back-scattering, sbsp
Light extinction, sext = ssp + sap
Number concentration, NCN
20 Mm-1 ~ 7 mg/m3 PM2.5 ~ 120 miles visibility
100 Mm-1 ~ 33 mg/m3 PM2.5 ~ 24 miles visibility

## Slide 29
Visibility  How far one can see (distance)
Light extinction inversely proportional to 1/visibility  1/distance
Rocky Mountain National Park http://vista.cira.colostate.edu/views/
Mm-1 - What are these weird units?
sext = 20 Mm-1
sext = 200 Mm-1
Distance unit conversions  1000 m = 1 km = 0.001 Mm
(130 miles visibility)
(12 miles visibility)