## Slide 1
Aerosol optical properties during fresh and aged wildfire smoke events in Colorado
July 2021, New York City
October 2020, Boulder CO
Elisabeth Andrews1, Lauren Schmeisser1, Patrick Sheridan1, Gannet Hallar2, Dan Jaffe3, James Sherman4
1NOAA, 2University of Utah, 3University of Washington, 4Appalachian State University
CSIRO, November 2022
Table
Mountain

## Slide 2
Motivation
Wildfires are predicted to increase with climate change (Jones et al., 2020).
Decrease air quality both near the fires and further away.
Understanding smoke properties and how they change with time:
  improve AQ models
  improve satellite detection algorithms

## Slide 3
Atmospheric monitoring building at Table Mountain
NOAA Federated Aerosol Network
~30 sites around world
NOAA’s Table Mountain atmospheric monitoring site
WPB
NOAA Federated Aerosol Network (NFAN) in US
WMO/GAW
What can we learn about smoke aerosol from NFAN measurements in the US?
NFAN overview: Andrews et al., BAMS, 2019
Notes: *WPB added in this year

## Slide 4
T640
All instruments located inside aerosol building at BOS
Sample from common inlet/flow splitter
Measurements made at low RH < 40%
Measurement start: September 2019
Analysis uses hourly-averaged data
Nephelometer – 3-l aerosol scattering
CLAP – 3-l aerosol absorption
Aethalometer – 7-l aerosol absorption
CPC – number concentration
DMPS – number size distribution (10-800 nm)
T640 – aerosol mass concentration (PM1, PM2.5, PM10)
Ozone monitor – surface O3 concentration
Picarro – CO, CO2, CH4, water vapor
Aerosol sampling at Table Mountain (BOS) facility north of Boulder
NEPH
CLAP
Inlet/
splitter
CPC
DMPS
Aeth
O3
Picarro
CO, CO2, CH4, H2O
BOS measures day/night, rain/cloud
Sampling at BOS started September 2019

## Slide 5
Absorption, scattering coefficients highest in summer
Range is ~3 orders of magnitude
Similar temporal pattern
Number Concentration
Aerosol Absorption Coefficient
Aerosol Scattering Coefficient
Aerosol time series at Table Mountain (BOS) – Aerosol amount
Note: y-axes are log scale
Covid
lockdown
Aerosol number concentration does NOT peak during smoke events
Time series not long enough to identify a Covid lockdown effect
Scattering when no smoke <30 Mm-1
Notes: Range in absorption & scattering is ~3 orders of magnitude
Range in number concentration is ~2 orders of magnitude

## Slide 6
2019
2020
2021
2022
Winter and spring exhibit approximately same scattering and absorption each year.
Interannual variability in absorption and scattering coefficients driven by fire influence.
2019 – No significant fire impact
2020 (Aug-Nov) - Local and regional fires
2021 (June-Sept) – Regional fires
2022 – No significant fire impact
SSA is higher during fire impacted periods – more reflective aerosol
BFR is clearly lower during fire impacted periods – shift to larger accumulation mode particles
Scattering and absorption Angstrom exponents are also higher during fire impacted periods (not shown) – suggests change in size and composition.
Aerosol interannual variability at Table Mountain (BOS)
Absorption coefficient
Scattering coefficient
Single scattering albedo
Backscatter fraction
August is most impacted month.
Notes: uses CLAP data for absorption,

## Slide 7
Differences in smoke sampled in 2020 and 2021 at Table Mountain
July 2020-Oct 2021
Scattering coefficient
smoke: scattering > 100 Mm-1
Can we identify smoke events based on aerosol characteristics?
Are there differences in aerosol properties for different smoke events?
  interpret/validate satellite retrievals
  Evaluate air quality models simulations
2020
local and long range smoke transport
2021
dominated by long range smoke transport from US west coast
No smoke: scattering < 30 Mm-1
Notes: zoom in on smoke events. In what follows will first look at how smoke differs from non-smoke and then will try to identify different types of smoke. need more tools than just amount!

## Slide 8
Scattering < 30 Mm-1 (no smoke)
30 < Scattering < 50 Mm-1 (minimal smoke)
50 < Scattering < 100 Mm-1 (some smoke)
Scattering > 100 Mm-1 (smoke!)
Shift in aerosol characteristics with increasing amount of aerosol (smoke) at BOS
Composition:
Less absorbing
More organic
Size:
Dominated by sub-um particles
Large sub-um particles
less absorbing
More sub-um
More organic
larger sub-um
Single scattering albedo
Scattering Angstrom Exponent
Absorption Angstrom Exponent
Backscatter fraction
Aerosol properties co-vary as smoke influence increases.
Can we learn more by studying co-variability of aerosol properties?
Frequency of Occurrence
Notes: so we see that some aerosol characteristic appear to be co-varying. can we use that systematic variability to look at the data in a different way? uses aeth for AAE and SSA

## Slide 9
Colored by SSA, 0.88<SSA<0.92
Colored by BFR, 0.12<BFR<0.20
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
Plots for scattering <30 Mm-1 – no smoke
Table Mountain aerosol generally falls in the BC region of the matrix.
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
Cappa 2016 matrix for insitu
dust
strong BrC
dust
Scattering Angstrom exponent vs Absorption Angstrom exponent at BOS (no smoke)
Scattering Angstrom exponent
Absorption Angstrom exponent
Scattering Angstrom exponent
Absorption Angstrom exponent
strong BrC
0.82
0.84
0.86
0.88
0.90
0.92
0.94
0.96
0.98
0.06
0.08
0.10
0.12
0.14
0.16
0.18
0.20
0.22

## Slide 10
Colored by SSA
Colored by BFR
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
dust
strong BrC
dust
Scattering Angstrom vs Absorption Angstrom exponent at Table Mountain
more absorbing particles
smaller sub-um particles
Scattering Angstrom exponent
Absorption Angstrom exponent
Scattering Angstrom exponent
Absorption Angstrom exponent
strong BrC
Smoke aerosol mostly falls in different sector than ‘normal’ aerosol - more BrC.
When it overlaps ‘normal’ aerosol, smoke properties are different (smoke BFR lower & SSA higher)
0.06
0.08
0.10
0.12
0.14
0.16
0.18
0.20
0.22
0.82
0.84
0.86
0.88
0.90
0.92
0.94
0.96
0.98

## Slide 11
Colored by SSA
Colored by BFR
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
dust
strong BrC
dust
Scattering Angstrom vs Absorption Angstrom exponent at Table Mountain
more absorbing particles
smaller sub-um particles
Scattering Angstrom exponent
Absorption Angstrom exponent
Scattering Angstrom exponent
Absorption Angstrom exponent
strong BrC
Is plume age a reason for the different smoke data clusters?
BFR<0.12
BFR>0.14
SSA>0.92
SSA<0.90
dust
dust
0.06
0.08
0.10
0.12
0.14
0.16
0.18
0.20
0.22
0.82
0.84
0.86
0.88
0.90
0.92
0.94
0.96
0.98

## Slide 12
AGED:
Scattering > 100 Mm-1
Bfr<0.13
Can we come up with fresh vs aged smoke algorithm for longer Table Mountain time series?
Fresh smoke vs ‘Aged’ smoke at Table Mountain
Correctly identifies 2020 fresh and aged events
Correctly identifies 2021 smoke as aged
FRESH:
Scattering > 100 Mm-1
Bfr>0.13
Scattering coefficient

## Slide 13
BOS: 2020-2021 data
Does smoke identification algorithm work across NFAN sites?
Fresh and aged smoke at Table Mountain are (mostly0 in same position in AAE vs SAE matrix
Troubling – March 20, 2021 event looks different.
Where do other sites fit on matrix?

## Slide 14
missing
Does smoke identification algorithm work across NFAN sites?
In 2021 all 5 sites were impacted by smoke.
MBO and SPL sampled both fresh and aged smoke
BOS, BND and APP sampled long range aged smoke.

## Slide 15
missing
Algorithm:
MBO and SPL sampled fresh and aged smoke
BOS, BND, APP sampled aged smoke
AGED
FRESH
Compare with NAAPS model
Does smoke identification algorithm work across NFAN sites?
Algorithm is promising for smoke age identification…

## Slide 16
MBO
SPL
Scattering (Mm-1)
https://www.nrlmry.navy.mil/aerosol
BOS
Morgan Creek fire
MBO
SPL
BOS

## Slide 17
MBO
SPL
BOS
https://www.nrlmry.navy.mil/aerosol
Still seems promising for smoke age identification…
How does the matrix look?
MBO
SPL
BOS

## Slide 18
BOS: 2020-2021 data
5 sites: 2021 data
Does smoke identification algorithm work across NFAN sites?
Not so good!!

## Slide 19
Different pattern across NFAN sites.
SAE appears to separate fresh vs aged: SAE>2 fresh smoke
Note: y-axis goes to 4 not 3
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
Absorption Angstrom exponent
strong BrC
small particles
low absorption
Does smoke identification algorithm work across NFAN sites?
Algorithm needs more work!

## Slide 20
Smoke algorithm considerations
Contributions from non-smoke aerosol more significant at BND, APP
Fires have different fuel types (grasses, trees, houses …)
Fires burn with different efficiency
Atmospheric conditions during transport may be different  different processing
Difficult to define ”smoke”
Problem for remote sensing identification of smoke:
rely on assumed aerosol properties
non-continuous so evolution might be missed

## Slide 21
Take-aways
NFAN measurements provide opportunity to study smoke aerosol optical properties across US.
At BOS, the interannual variability in aerosol amount appears to be driven by smoke events.
Smoke aerosol is clearly different from the ‘normal’ aerosol
Size (more accumulation mode particles, dominated by sub-um particles)
Less absorbing
More organic
Working on algorithm to identify fresh vs aged smoke across NFAN network
Table Mountain algorithm doesn’t work at other NFAN sites
in progress…
Combined surface and satellite measurements may improve smoke identification (ongoing)

## Slide 22
Continuous long-term aerosol observations are essential
Foundation for describing aerosol climatology
  Recognize anomalous aerosol events
  Identify trends (e.g., if there is a ‘new normal’ due to more fires)
  Unique and important dataset for evaluating models and satellite observations
Future vision
  Expanded and collocated measurement network to increase spatial coverage, particularly in the southwest U.S.
  Mobile laboratory to make targeted measurements of smoke plumes and other extreme aerosol events
Big Picture and Future Vision
Baylor University mobile aerosol trailer
NFAN
Proposed

## Slide 23
Questions???

## Slide 24
extra slides

## Slide 25
News articles this week!

## Slide 26
Backscatter fraction (BFR)
Scattering Ångström exponent (SAE)
Absorption Ångström exponent (AAE)
Single scattering albedo (SSA)
Derived aerosol optical properties
Angular dependence of scattering
wavelength dependence of scattering
Independent of amount of particles – dimensionless
Useful for comparing different sites, events
Provide information about particle ‘nature’ (chemistry/microphysics)
Relative amount of absorption
wavelength dependence of absorption
SIZE
COMPOSITION
Do the aerosol properties for smoke differ from those of background air?
Notes: not sure how familiar you are with these turms

## Slide 27
August (smoky month)
highest SSA
highest AAE
highest SAE
lowest BFR
Smoke Composition:
Less absorbing (SSA)
More organic (AAE)
Smoke Size:
Dominated by sub-um particles (SAE)
Shift in accumulation mode to larger sub-um particles (BFR)
Aerosol ‘characteristics’ monthly climatology at Table Mountain (BOS)
Single scattering albedo
Absorption Angstrom
Scattering Angstrom
Backscatter fraction
Notes: interesting that 95 percentiles aren’t so clearly different in fire months. note: using clap for SSA and AAE not AETH

## Slide 28
Monthly aerosol climatology at Table Mountain (BOS) facility north of Boulder
Number concentration
Absorption coefficient
Scattering coefficient
Scattering and absorption in summer and fall are impacted by fires (especially August)
Fire impact visible in the 95th percentiles in scattering and absorption coefficient
Number concentrations are higher in springtime – no clear fire influence
95th percentile
75th percentile
Median
25th percentile
5th percentile
How consistent is this seasonal pattern?
September 2019 – May 2022

## Slide 29
Nov-Feb
Mar-May
Jun-Jul
August
Sep-Oct
Aerosol size distribution monthly climatology at Table Mountain (BOS)
***RAW*** median aerosol size distribution data
August aerosol size distribution very different
More particles in accumulation mode.
Makes sense that calculated parameters related to size (BFR and SAE) are different for smoke events.

## Slide 30
Scattering < 30 Mm-1 (no smoke)
30 < Scattering < 50 Mm-1 (minimal smoke)
50 < Scattering < 100 Mm-1 (some smoke)
Scattering > 100 Mm-1 (smoke!)
Shift in aerosol characteristics with increasing amount of smoke at BOS
Smoke composition:
Less absorbing
More organic
Smoke size:
Dominated by sub-um particles
Larger sub-um particles
less absorbing
More sub-um
More organic
larger sub-um
Pink dots represent median of March 2021 mystery peak
suggests it could be smoke
Single scattering albedo
Scattering Angstrom Exponent
Absorption Angstrom Exponent
Backscatter fraction
Frequency of Occurance
Notes: so we see that some aerosol characteristic appear to be co-varying. can we use that systematic variability to look at the data in a different way? uses aeth for AAE and SSA

## Slide 31
https://www.nrlmry.navy.mil/aerosol
Scattering coefficient
??
20 March
https://www.nrlmry.navy.mil/aerosol
NAAPS model
fire location from MODIS satellite retrievals
Smoke near Table Mountain on March 20, 2021.
March 20 comparison with NAAPS model prediction
NAAPS = Navy Aerosol Analysis and Prediction System

## Slide 32
Cazorla et al., 2013
Using systematic variability to identify aerosol type
Co-variability of aerosol properties can provide more detailed information about aerosol type or composition.
Cappa et al., 2016
Column SAE
Scattering Angstrom exponent
Absorption Angstrom exponent
column AAE
combine with next?

## Slide 33
Remote sensing
In-situ
Using systematic variability to identify aerosol type
Systematic relationships can provide information about particle types and processes
changes in source
atmospheric processing
(Hallar et al., ACP, 2015)
Note: SPL is 150 km NW of Table Mountain
Angstrom Exponent
Angstrom Exponent
AOD
Scattering coefficient
Smoke and dust exhibit different co-variability
Storm Peak Laboratory, CO
Storm Peak Laboratory, CO
Notes: simple way is plotting amount vs an aerosol characteristic kind of like we did in last plots. here see amount vs SAE and that known aerosol events (dust and smoke) look different. See this both in remote sensing data (left) and in-situ data (right).

## Slide 34
Using systematic variability to identify aerosol type at Table Mountain
Storm Peak Laboratory, CO
Table Mountain, CO
scattering > 100 Mm-1
Scattering Angstrom exponent increases with scattering during smoke events
Table Mountain doesn’t exhibit a clear dust signal.
Notes: Plots cover different time periods for the 2 sites
Scattering Angstrom Exponent
Scattering coefficient
Scattering Angstrom Exponent
Scattering coefficient
Notes: But – can also look at relationships between aerosol characteristics which might be more interesting/enlightening

## Slide 35
Fresh local smoke plumes Aged long range transport smoke
Scattering coefficient
1-Sept
15-Sept
Fresh smoke vs ‘Aged’ smoke at Table Mountain
In 2020 Table Mountain sampled both fresh and aged smoke.
Fresh smoke often came from less than 100 km away.
BOS
8-Sept
22-Sept
1-Oct
8-Oct
15-Oct
Date, 2020

## Slide 36
Smoke was observed across US in 2021
Aerosol scattering coefficient
Aerosol scattering levels were 5-50x higher than ‘normal’ during some smoke events.
NOAA Federated Aerosol Network (NFAN) in US

## Slide 37
Fresh local smoke plumes Aged long range transport smoke
Scattering coefficient
Fresh smoke in BrC sectors
Aged smoke crosses BC/BrC sectors
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
BC/large particles
large particles
low absorption
strong BrC
Fresh smoke vs ‘Aged’ smoke at Table Mountain
1-Sept
15-Sept
8-Sept
22-Sept
1-Oct
8-Oct
15-Oct
Date, 2020
Fresh and aged smoke events appear in different places on AAE vs SAE matrix
In 2020 Table Mountain sampled both fresh and aged smoke.
Fresh smoke often came from less than 100 km away.

## Slide 38
something about satellite smoke masks? lauren stuff.
Improving satellite identification of smoke events
Surface smoke events
Time series of scattering at BOS from nephelometer
Yellow dots smoke events
(scat > 100 Mm-1)
Do different methods all identify the same smoke events?
(work by Lauren Schmeisser)

## Slide 39
Identification of smoke events at Table Mountain
All three methods identify smoke
Surface methods see smoke, satellite does not
Identification of smoke event changes with method.
Triangles indicate smoke identified and
are at satellite retrieval times.
In-situ from nephelometer at surface.
Satellites are NOAA-20 (J01) and NPP.
AOD from MFRSR at surface.
Surface smoke events

## Slide 40
Identification of smoke events at Table Mountain
All three methods identify smoke
Surface methods see smoke, satellite does not
Surface smoke events
BOS

## Slide 41
Identification of smoke events at Table Mountain
All three methods identify smoke
Surface methods identify smoke, satellite does not
Surface smoke events
BOS
Satellite gridding might cause smoke identification algorithm to miss smoke
Or assumptions about smoke properties? (We know they change!)
Or ???
Ongoing research!

## Slide 43
Collaud Coen et al., JGR, 2007
Wavelength dependence of scattering is function of particle diameter
Backscattering fraction (BFR) most affected by particles<0.3 um
Scattering Ångström exponent (SAE) by particles>0.5 um
Derived aerosol optical properties
450 nm
550 nm
700 nm
0.01 0.1 1.0 10
Diameter (um)
BFR
SAE
Backscatter fraction and scattering Ångström exponent
Scattering efficiency
Diameter (um)

## Slide 44
Collaud Coen et al., JGR, 2007
Wavelength dependence of scattering is function of particle diameter
Scattering Ångström exponent (SAE) most affected by particles> 0.4-0.5 um
Derived aerosol optical properties
450 nm
550 nm
700 nm
Scattering Ångström exponent (SAE)
Scattering efficiency
SAE = - log(scat(l=450)/scat(l=700))
log(450/700)

## Slide 45
Scattering Angstrom Exponent (SAE)
Derived aerosol optical properties
Volume (fine)/Volume (total)
SAE >2  mostly small particles
SAE < 1  more big particles (dust, sea salt…)
Scattering Angstrom exponent
Schuster, JGR, 2006

## Slide 46
Backscattering fraction (BFR)
Smaller particles scatter light symmetrically.
Larger particles scatter more light forward than backward.
Backscattering fraction most affected by particles < 0.3 um
Derived aerosol optical properties
BFR=0.5
BFR=0.2
BFR=0.1
D=0.05 um
D=0.1 um
D=0.2 um
Other aerosol parameters related to backscatter fraction include upscatter fraction and asymmetry parameter.
BFR = backscatter
total scatter

## Slide 47
0.3 < SSA < 1  typical atmospheric values ~0.8-0.9
SSA ~ 0.4
SSA ~ 0.8
SSA ~ 1.0
Single Scattering Albedo (SSA)
Atmospheric particles can be mixtures of absorbing aerosol (black carbon) and scattering aerosol.
Particles with relatively more absorbing aerosol will have lower SSA.
Derived aerosol optical properties
SSA = scatter
scatter+absorb

## Slide 48
Russell et al., ACP, 2010
Absorption Angstrom exponent increases with organic mass fraction.
Derived aerosol optical properties
Absorption Angstrom Exponent (AAE)
Black Carbon AAE = 1
Particle with lots of organic
AAE = 3
AAE = - log(abs(l=450)/abs(l=700))
log(450/700)

## Slide 49
Smoke Size:
Dominated by accumulation
Scattering < 30 Mm-1 (no smoke)
30 < Scattering < 50 Mm-1 (minimal smoke)
50 < Scattering < 100 Mm-1 (some smoke)
Scattering > 100 Mm-1 (smoke!)
‘No smoke’ looks like annual median size distribution
Smoke size distribution is very similar to August size distribution
Shift in aerosol size distribution with increasing amount of smoke at BOS
Nov-Feb
Mar-May
Jun-Jul
August
Sep-Oct

## Slide 50
= f(aerosol amount, backscatter fraction, single scattering albedo)
Aerosol
Radiative
Forcing
https://www.earthdata.nasa.gov/learn/find-data/near-real-time/firms/active-fire-data
satellite

## Slide 51
Smoke Composition:
Less absorbing
More organic
Smoke Size:
Dominated by sub-um particles
Shift in accumulation mode to larger sub-um particles
Fresh
Aged
Dg~0.17 um
Dg~0.27 um

## Slide 52
something about smoke age?
start with 2020 and lauren’s dates and time series then SAE vs AAE
small particles
low absorption
mixed BC/BrC
BC dominated
dust/BC/BrC
large particles
low absorption
strong BrC
dust
AGED:
Scattering > 100 Mm-1
Bfr<0.13
FRESH:
Scattering > 100 Mm-1
Bfr>0.13
Scattering Angstrom exponent
Absorption Angstrom exponent
March 20 event
Why would fresh have more BrC??

## Slide 53
Notes: uses CLAP data for SSA and AAE

## Slide 54
Two populations in scat10/PM10 plot
Population#1 (smoke-influenced?):
High scattering: >50 Mm-1
SSA >0.92
BFR<0.12
1.75<SAE<2.0
AAE>1.5
Population#2 (“normal”)
SSA<0.92
BFR>0.12
SAE<1.5
1.0<AAE<1.75
smoke
high loading smoke aerosol exhibits different scat10/PM10 relationship than other aerosol
Relationship between scat10 and PM10 as function of AOPs
PM10
PM10
PM10
PM10

## Slide 55
colored by BFR
colored by AAE
colored by SSA
Other systematic relationships
Best for separating smoke
scat<30 Mm-1
scat>100 Mm-1
skip?? and go into smoke age?

## Slide 56
BFR
CN
AAE
SAE
SSA
AAE
CN
SAE
SSA
BFR
SSA
CN
AAE
SAE
BFR
SAE
SSA
BFR
AAE
CN

## Slide 57
AAE
SAE
SSA
Scat
o3
CO
what are brown points?
fix labels, axis (set xticks),
smaller symbols? or have later symbols in loop be smaller so can see earlier symbols?

## Slide 58
ranges from 0.1-0.7 (I think it’s delta o3 and delta co), o3-35/CO-100 should increase with plume age
NOT SURE WHAT SHOULD USE AS BASELINE O3 – 30? 35? 40?
jaffe 2012 – modified combustion efficiency MCE = co2/(co+co2) 0.92 temperate, 0.80 boreal
increase with age
decrease with age
AAE
SAE
SSA
Scat
o3
CO

## Slide 59
Ozone increases with smoke
Scattering < 30 Mm-1 (no smoke)
30 < Scattering < 50 Mm-1 (minimal smoke)
50 < Scattering < 100 Mm-1 (some smoke)
Scattering > 100 Mm-1 (smoke!)
Ozone lower in fresh smoke than aged smoke
aged
fresh
aged
fresh
However, a smaller number of studies, mainly in boreal regions, have found that O3 is minimally enhanced or even depleted downwind of some biomass burning plumes (e.g. Tanimoto et al., 2008; Paris et al., 2009; Verma et al., 2009; Alvarado et al., 2010). The low O3 production in these plumes was likely caused by low mixing ratios of NOx due to low emissions, sequestration of NOx as PAN, and/or a reduction in photochemical reactions (especially due to aerosol effects).
aged
fresh
color by something else? BFR?
o3/co ratio? which should increase with age

## Slide 60
Scattering < 30 Mm-1 (no smoke)
30 < Scattering < 50 Mm-1 (minimal smoke)
50 < Scattering < 100 Mm-1 (some smoke)
Scattering > 100 Mm-1 (smoke!)
aged
fresh
aged
fresh
CO increases with smoke
CO higher with fresh, but also lower at scat=50 Mm-1 level

## Slide 61
Fine mode:
inorganic ~2.6 m2/g
organic ~3.9 m2/g
mixed~3.6 m2/g
biomass smoke > 6 m2/g
dust ~3 m2/g
Coarse mode
mixed ~1 m2/g
dust ~0.7 m2/g
smoke ---
y=2.87*m+8.03, R2=0.80
y=1.15*m+1.47, R2=0.51
MSC values from Hand et al., 2007
Mass Scattering Coefficient (MSC) at Table Mountain
y=3.81*m-3.00, R2=0.98
Table Mountain aerosol does NOT exhibit increase in MSC for fine biomass smoke
MSC ~3.8 m2/g
Table Mountain does exhibit increase in MSC for coarse biomass smoke
MSC ~2.9 m2/g
PM1 scattering (Mm-1)
PM10 scattering (Mm-1)
PM1 mass conc (ug/m3)
PM10 mass conc (ug/m3)
MSC = scattering coefficient
mass concentration

## Slide 62
Mass Absorption Coefficient (MAC) at Table Mountain
Don’t have reference measurement of absorbing aerosol mass
Can bound the range of MAC at Table Mountain based on literature
MAC =absorption coefficient
BC mass concentration
pure BC MAC=7.5 m2/g
(Bond&Bergstrom, 2006)
5.8
abs
CO
BC
CO
*
1
MAC
=
smoke
Spackman et al., 2008
MAC~7.5 m2/g
MAC~23 m2/g
smoke MAC=26m2/g
(Mason et al., 2018)
Which absorption coefficient: CLAP or Aeth?
Where is CO2 data?
Notes: at BOS MMR is approx same as mass conc:
mass conc=MMR*p/RT, R=287J/kg-K, T=298K, P=85000 N/m2=85000=85000J/m3