## Slide 1: NOAA ESRL GMD Carbon Cycle GHG Measurement Program
Ed Dlugokencky

## Slide 2: Projects
Tall towers - N American focus
Aircraft Vertical Profiles - N American focus
Observatory - Global background focus
Cooperative global air sampling network
  Constrain large scale GHG budgets
  Weekly discrete air samples
  Analyzed in Boulder
    CO2 (+iso), CH4 (+iso), N2O, SF6, CO, H2
    Suite of ODSs (PFPs (i.e., tower and VP) only)
    Suite of NMHC (CU INSTAAR)

## Slide 4
Analytical |  |  | 
Species | Current Χ | Technique | Repeatability
CO2 | 400 ppm | NDIR | 0.03 ppm
CH4 | 1900 ppb | GC/FID | 1.0 ppb
N2O, SF6 | 328 ppb 8.8 ppt | GC/ECD | 0.3 ppb, 0.03 ppt
CO | 100 ppb | VUV-RF | 0.7 ppb
H2 | 500 ppb | GC/PD-HeID | 0.3 ppb
*δ13CO2 | -8.5‰ | IRMS | 0.01‰
*δ13CH4 | -47.2‰ | GC/IRMS | 0.04‰
Quantity: “amount of substance ratio”
Unit: dry-air mole fraction
*University of Colorado, INSTAAR; isotope ratios in “per mille”

## Slide 5
Analysis of flask-air filled from a calibrated cylinder
±0.1 ppm
-0.06 ± 0.12 ppm (entire record)
-0.03 ± 0.06 ppm (since 2000)
Quality Control

## Slide 6
Co-located comparison at Mauna Loa
How well do we propagate our standard scale?
Flask minus Continuous
0.04 ± 0.27 ppm (entire record)
0.07 ± 0.13 ppm (since 2000)

## Slide 7
Comparison with other labs at NOAA site: Mauna Loa

## Slide 8
Quality Control
Comparison of NOAA and EC data at ALT

## Slide 9
Complementary comparisons
Detecting problems using other species
Courtesy: Steve Montzka
H-1211
HFC-134a
Data courtesy of
A. Andrews (NOAA)
Flask minus Continuous

## Slide 10
Barrow, Alaska

## Slide 13
[CH4](t) = [CH4]ss-([CH4]ss-[CH4]0)e-t/τ
Lifetime ≈ 9.4 yr

## Slide 14
Average Emissions = 550 ± 13 Tg CH4
Trend = 0 ± 0.6 Tg CH4 yr-1
Lifetime () = 9.1 yr
Emissions = d[CH4]/dt + [CH4]/

## Slide 15
Pinatubo and Chemistry (Largest term in CH4 budget)
OH + CH4 → CH3 + H2O
O3 + hν (330 ≥ λ ≥ 290 nm) → O(1D) + O2
O(1D) + H2O → 2 OH
Rate of formation O(1D) = j [O3]
j = ∫F(λ) σ(λ) φ(λ) dλ
Also affected CO

## Slide 16
AI < 0.1 means clear sky; AI > 4 obscures mid-day sun
Eruption of Mt. Pinatubo: 15 June, 1991

## Slide 17
O3 + hν (330 ≥ λ ≥ 290 nm) → O(1D) + O2
O(1D) + H2O → 2 OH
Rate of formation O(1D) = j [O3]

## Slide 18
Globally averaged CH4 and δ13C(CH4)
Sylvia Michel, INSTAAR

## Slide 20
SOI: Australian BoM
Precipitation anomalies in tropical wetlands. (Source: GPCP)
Increased Amazon CH4 fluxes in wet years.
Consistent with decrease in δ13C of CH4

## Slide 21
Late-1990s - mid-1980s
Interpolar difference (53-90°)
No measureable change in Arctic CH4 emissions.

## Slide 22: Summary
NOAA’s Global Cooperative Air Sampling Network is invaluable for understanding large scale features of global budgets of LLGHGs
No trend in total global emissions 1984-2006
Change in budget since 2007
Much to learn studying IAV

## Slide 24
AF ~ 45% (trend ≡ -0.16)
Suggests increasing sink
CO2 - Constraining its budget