## Slide 1: NOAA Carbon Cycle GHG Measurement Programs
Ed Dlugokencky

## Slide 2: Projects
Tall towers - N American focus
Aircraft - N American focus
Observatory - Global background focus
Cooperative global air sampling network
  Constrain large scale GHG budgets
  Weekly discrete air samples
  Analyzed in Boulder
    CO2 (+iso), CH4 (+iso), N2O, SF6, CO, H2
    Suite of NMHC

## Slide 4
Analytical |  |  | 
Species | Current Χ | Technique | Repeatability
CO2 | 407 ppm | NDIR | 0.06 ppm
CH4 | 1900 ppb | GC/FID | 1.0 ppb
N2O, SF6 | 330 ppb 9.3 ppt | GC/ECD | 0.3 ppb, 0.03 ppt
CO | 100 ppb | VUV-RF | 0.7 ppb
H2 | 500 ppb | GC/PD-HeID | 0.3 ppb
*δ13CO2 | -8.5‰ | IRMS | 0.01‰
*δ13CH4 | -47.3‰ | GC/IRMS | 0.04‰
Quantity: “amount of substance ratio”
Units: dry-air, mole fraction
*University of Colorado, INSTAAR; isotope ratios in “per mille”

## Slide 5: Sampling at BKT
Started in January, 2004
  Always a difficult site for CO and CO2
  Data for CH4 and other species are good
Terminated in February, 2011
  Drastic cut in NOAA funding resulted in many sites being terminated
Restarted in February, 2013
  With urging from BMKG
  Problematic for CO2 at start-up
  Significantly improved, since

## Slide 6
BKT

## Slide 7
Volcanic emission?

## Slide 8
Low P in some samples during analysis; much improved since 2015.
Please write observer’s name, flow rate, V, and P on sample sheet.
Pressure (psia)

## Slide 10
[CH4](t) = [CH4]ss-([CH4]ss-[CH4]0)e-t/τ
Lifetime ≈ 9.2 yr

## Slide 11
Average Emissions = 550 ± 13 Tg CH4
Trend = 0 ± 0.6 Tg CH4 yr-1
Lifetime () = 9.1 yr
Emissions = d[CH4]/dt + [CH4]/

## Slide 12
Globally averaged CH4 and δ13C(CH4)
Sylvia Michel, INSTAAR

## Slide 13
Pinatubo and Chemistry (Largest term in CH4 budget)
OH + CH4 → CH3 + H2O
O3 + hν (330 ≥ λ ≥ 290 nm) → O(1D) + O2
O(1D) + H2O → 2 OH
Rate of formation O(1D) = j [O3]
j = ∫F(λ) σ(λ) φ(λ) dλ
Also affected CO

## Slide 14
AI < 0.1 means clear sky; AI > 4 obscures mid-day sun

## Slide 15
O3 + hν (330 ≥ λ ≥ 290 nm) → O(1D) + O2
O(1D) + H2O → 2 OH
Rate of formation O(1D) = j [O3]

## Slide 17
AF ~ 45%
CO2 - Constraining its budget

## Slide 18
www.esrl.noaa.gov/gmd/ccgg/carbontracker/

## Slide 19
www.esrl.noaa.gov/gmd/ccgg/carbontracker/

## Slide 22: Summary
We (NOAA and BMKG) collaborate to produce data that provide the strongest constraints on LLGHG emissions
NOAA thanks BMKG for their continued collaboration
Questions?