## Slide 1
Operation and application of aerosol measurement system –
Temporal, spatial and systematic patterns in aerosol properties at Anmyeon-do (AMY)
Dr. Elisabeth (Betsy) Andrews
NOAA/ESRL/Global Monitoring Division
Boulder, CO USA
November, 2013

## Slide 2
Talk Outline
Overview of NOAA collaborative aerosol network
Description of collaborative aerosol measurements at Anmyeon-do (AMY)
Temporal climatology of aerosol properties at AMY
Systematic relationships between aerosol properties at AMY
Preliminary air mass analysis and relationship to aerosol properties at AMY
Future work

## Slide 3
Motivation and collaborative network picture
Detect changes (i.e., trends, cycles) in the long-term global aerosol background
Characterize climate-forcing properties of aerosol types on regional scales
Original 4 NOAA baseline observatories
6 NOAA observatories
18 collaborations (including AMY!)

## Slide 4
Advantages of a Collaborative Network
Ensure measurement comparability – measurements made the same way
Economies of time and scale – no need to reinvent the wheel
Climate forcing and climatology as a function of location
Satellite and Model evaluation/validation
Long term (>10 years) trends
changes due to pollution control policies
climate change
Spatial/Temporal variability studies
useful for comparing data on different time or spatial scales, e.g.,
model grid vs point measurement
satellite AOD vs surface AOD
Examples of science that can be done with network data

## Slide 5
Polar
Marine
Mountain
Continental
Polar
Marine
Mountain
Continental
Annual climatology from the NOAA collaborative network
AMY
GSN
aerosol amount
visibility
Aerosol optical depth (AOD)
Relative amount of absorption
NOAA sites
Collaborators
Closed sites

## Slide 6
Autocorrelation Analysis – Marine sites
Compares “persistence” - i.e., how quickly a property changes with time.
Useful when trying to compare measurements on different temporal or spatial scales.
day
week
month
year
Correlation coefficient r(k)
Example: comparing night time aerosol measurements from a satellite with daytime measurements from AERONET sensor
t=0
t=12

## Slide 7
Particle counter
(number concentration)
Absorption
Photometer
(spectral absorption)
Nephelometer
(spectral scattering and backscattering )
Switched Impactors
(Dp<10 mm and Dp<1 mm )
Ångström Exponents, Asymmetry Parameter, Single Scattering Albedo, Radiative forcing
KMA/DUST aerosol system at AMY
Same design at NOAA sites and collaborator sites
Follow GAW protocols

## Slide 8
aerosol single scattering albedo
(from nephelometer and PSAP)
average aerosol up-scatter fraction
(from nephelometer backscatter fract)
D daylight fraction
S0 solar constant
Tat atmospheric transmission
Ac cloud fraction
Rs surface albedo
Parameters controlling aerosol forcing
Source: Haywood and Shine (1995)
DF average aerosol forcing at top of atmosphere (TOA)
d aerosol optical depth
DF/d = Top of Atmosphere Radiative Forcing Efficiency

## Slide 9
Intensive Properties – depend on character of aerosol:
Absorption Angstrom exponent – ‘type’ of absorbing particles
AbsAngst ~ 1 suggests elemental carbon
AbsAngst >1 suggests organics
AbsAngst >1.5 + SSA increasing with wavelength suggests dust
AbsAngst < 1 suggest BC core with coating
Scattering Angstrom exponent - size of particle
ScatAngst < 1.5 suggests dust (or sea salt)
ScatAngst > 2 suggests pollution aerosol
Parameters from aerosol system
Extensive Properties – depend on amount of aerosol:
Scattering
Absorption
Extinction (= scattering + absorption)
Number concentration (CN)

## Slide 10
Diurnal climatology at AMY (Nov 2011 – Sept 2013)
Notes:
Extinction=scattering+absorption
Box-whiskers represent 5th, 25th, median (50th), 75th and 95th percentiles.
Time is in UTC, vertical yellow bar indicates local noon.
Measurements are made at low RH and have standard corrections applied.
Minor diurnal variation observed in some aerosol properties
Notes: Not much diurnal cycle except in CN. Maybe also see it in back scatter fraction which is sensitive to smaller particles.

## Slide 11
Weekly climatology at AMY (Nov 2011 – Sept 2013)
Some weekly variation observed in aerosol properties
Timing of AMY extinction and absorption weekly cycle consistent with observations by Murphy et al. (2008) for multiple sites in US.

## Slide 12
Annual climatology at AMY (Nov 2011 – Sept 2013)
Possible seasonal patterns in aerosol extinction and absorption
more extinction in the summer?
more absorption in the winter?
Notes:
Data coverage: Winter (47%), Spring (70%), Summer (39%), Autumn (22%) (based on hourly extinction data)
Green box-whisker represents statistics for all QC’d data to present.
Suspect
CN data
Notes: Highest scattering and absorption observed in Jan and May. What could cause this? Dust?
Whiter aerosol in summer than winter. More local combustion in winter?
Also larger particles in summer – more (relative) contribution from sea salt?

## Slide 13
Annual climatology at AMY (Nov 2011 – Sept 2013)
More obvious seasonal variation in intensive properties:
suggests different sources and/or processes
what can other studies tell us about source types?
what can we learn from airmass trajectories?
Notes: Highest scattering and absorption observed in Jan and May. What could cause this? Dust?
Whiter aerosol in summer than winter. More local combustion in winter?
Also larger particles in summer – more (relative) contribution from sea salt?

## Slide 14
Based on AERONET data from many sites
column
ambient
wavelengths~ 440/870
AMY data in relation to aerosol ‘type’ matrices
Single Scattering Albedo
Absorption Angstrom
Extinction Angstrom
Extinction Angstrom
Plots are from Giles et al., 2012
Dot ( ) shows AMY in-situ median
in-situ
dry conditions
wavelengths~ 450/700
Dot ( ) shows AMY AERONET median (2000-2007 data)
Plots suggest that AMY aerosol is most representative of either ‘urban/industrial’ or ‘mixed’ sources

## Slide 15
I
a
AMY data in relation to aerosol ‘type’ matrices
AMY in-situ median
in-situ
dry conditions
wavelengths~ 450/700
AMY AERONET median
(2000-2007 data)
AMY aerosol is most representative of EC/OCsources
I
a
Plot from Cazorla et al., 2013
Based on AERONET data
column
ambient
wavelengths~ 440/870
Differences between in-situ and AERONET data may be due to relative humidity, inlet inefficiency, wavelength differences, data times, etc.

## Slide 16
Aitkin
Soot
Biomass
Small Organic
Coarse Marine
Coarse Dust
Large Organic
Large Inorganic
I
AMY in-situ median values represented by large dot ( ).
AMY AERONET median values represented by large dot ( ).
(2000-2007 data)
The tees and crosses represent other studies. The studies most similar to the AMY points were of mixed aerosol and urban/industrial pollution aerosol.
I
a
a
AMY data in relation to aerosol ‘type’ matrices
Extinction Angstrom
D(Single scattering albedo)*Absorption Angstrom
Mixed:
soot+coarse
Plot from Costabile et al., 2013
Plot based on in-situ data using
same instruments as at AMY

## Slide 17
AMY data – Systematic Variability
Approach used by Delene and Ogren, 2002; Andrews et al., 2011
THD – clean marine
AMY– polluted marine
GSN – polluted marine
ARN – polluted marine
WLG – high altitude+dust
LLN – high altitude+BB
APP – rural continental
KPS – rural continental
Natural Grouping
continental (no dust)
Natural Grouping
polluted marine
Scattering Angstrom
Clean marine and dust environments are different from other sites and from each other
Smaller particles

## Slide 18
AMY data – Systematic Variability
Approach used by Delene and Ogren, 2002; Andrews et al., 2011
Absorption Angstrom
Scattering Angstrom
THD – clean marine
AMY– polluted marine
GSN – polluted marine
ARN – polluted marine
WLG – high altitude+dust
LLN – high altitude+BB
APP – rural continental
KPS – rural continental
Marine sites and Dust site:
Less absorption  bigger particles
More absorption
Smaller particles
Composition change
More absorption
Dust site clearly different than other sites, but all sites see changing composition

## Slide 19
5-day back trajectories files at 0, 12 UTC were generated by Dr. Sangsam Lee of KMA.
Clustering of trajectories:
Clusters based on latitude, longitude and altitude vectors of individual trajectories
k-means clustering (as implemented in IDL graphical programming language)
Minimizes variability within cluster, maximizes variability among clusters
Trajectory Clustering
Example output:
Latitude/Longitude mapping
Altitude time series
Black line is cluster median.

## Slide 20
Note:
‘annual’ covers Nov 2011-June 2012
Trajectory Clustering - Annual
39
89
90
133
103
Pink (low altitude) most common in warm season.
Green&Blue most common in cold season
Gray occurs throughout year

## Slide 21
Previous air mass analysis (Turnbull et al., 2011) for the Taean peninsula suggests:
Ann Win Sum
RPCN 60% 80% 40%
RPCS 5% 10%
LK 30% 40%
OBG 5% 10%
northern China (RPCN) is primary air mass source to Taean peninsula except in summer.
(Local)
(OceanBackground)
This is consistent with the Nov-June trajectory clustering results presented in this talk.
How do these trajectories compare?

## Slide 22
Most time under 1000 m
(pink)
high extinction
high single scattering albedo
low absorption Angstrom exponent
Trajectory Clustering - Annual
Most time above 2000 m
(green, yellow)
high number, low extinction
low single scattering albedo
high absorption Angstrom exponent
In between
(blue, gray)
similar and properties between high and low trajectories
None of these clusters have the typical characteristics of dust:
low scattering Angstrom < 1.5
high absorption Angstrom > 1.5

## Slide 23
Conclusions
Temporal aerosol property patterns
Aerosol property diurnal cycles are not particularly strong.
There is a weekend effect in some aerosol properties measured at AMY.
There are strong seasonal cycles in some aerosol properties suggesting the influence of different sources and/or processing.
Systematic aerosol property patterns
Comparison of AMY aerosol data to aerosol property matrices suggest the AMY air masses are dominated by urban/industrial pollution.
AMY has similar systematic variability as other polluted marine sites (ARN, GSN)
Spatial aerosol property patterns
Trajectory clustering shows:
winter air masses are primarily transported from NW (China, Mongolia, Russia)
warm season air masses are closer to surface and more often local
low altitude trajectories tend to have higher loading and whiter particles (possibly due to thick coatings on particles)
high altitude trajectories are cleaner, and darker (lots of EC+some organics?)
no obvious dust cluster in this analysis

## Slide 24
Future work
Near future:
revisit trajectory analysis with fuller data set
statistics – are the clusters properties really different?
Conference presentation? International Aerosol Conference (Busan, 2014)
Paper?
Far future:
long term trends (need ~10 years of data to do good trend analysis)

## Slide 25
Thank you!
Any Questions?

## Slide 26
Winter

## Slide 27
spring

## Slide 28
Clustered trajectories for Winter and Summer
(see difference between seasons, but waiting for more summer trajectory files!)
Winter (Dec 2011-Feb 2012
Summer  these trajectories are only for June 2012

## Slide 29
Any relationship between seasonality of aerosol properties and carbon cycle gases?
Difficult to assess because of gaps in data and protocols for gas sampling.